Energy Modeling Job Aide

- Project Assessment: Get to know the job

- Review the project file, plans, emails and any notes.

- Complete an intake form, being sure to confirm climate zone and zip code (required for HERS registration).

- Review the scope of work, clear up any questions and/or alternative compliance features/options, create talking points to have with client.

- Determine compliance path and goals.

  - What are the goals (min. compliance, Reach Code, Green Point Rated, LEED for Homes, PV electric usage summary, load calculations, etc.)?

  - What type of job is this? (New construction; Existing plus alteration (E+A); Existing plus alteration plus addition (E+A+A); Addition alone.

  - What compliance path will fit this job best (performance or prescriptive)?	Why?

- Gather and Organize Information: Project Take-Offs

  - Determine/map out zones.

  - Measure the area in square feet (SF) of conditioned versus unconditioned floor area, and exterior/demising floors, walls, roof/ceilings, windows, doors.

  - Write out the project areas by the zone and room. Use the Project Information Worksheet to gather and organize take-offs.

- Model the Project: EnergyPro or CBECC-Res

  - Model take offs (DHW, HVAC, Zones -- walls, floor, roof, windows, doors, orientation).

  - Run the model.

  - Use the Project Information Worksheet to verify modeling inputs (Look at the report for obvious errors such as rotation and number of bedrooms).

- Analysis and Review

- Use the Project Information Worksheet to review the Certificate of Compliance (CF1R) for input errors.

- Does the Model comply?

  - Yes, Review the report for errors and proceed in creating Energy Compliance Summary.

  - No. Make adjustments based on findings to get to compliance. Make one adjustment at a time, and keep a list of each item changed and the compliance model that resulted until you get a model that complies.

- Write up the Energy Features Summary.

| Single-Family INTAKE FORM TITLE 24 PART 6 ENERGY COMPLIANCE |
| --- |
| Bid: $ | Date In: | Date Out: | Job #: |
| Designer: | Owner: |
| Phone: E-Mail: | Phone: E-Mail: |
| Address: | Address: |
| Project Title: |
| Address: | City: | Zip code: | CZ: |
| City / Building Dept.: | Front Orientation: |
| Occupancy: Single family / ADU detached / ADU attached / Duplex / Townhome |
| Scope of work: New construction / single family addition / ADU addition / alteration |
| Year of Home/Major Upgrades (if existing): |
| Above Code (if applicable): GPR / LEED / Reach Code / Other: | Compliance Goal: |
| ENVELOPE ASSEMBLIES |
| Roof Type #1 (new/altered/existing condition to be HERS verified): Type (Attic, Rafter, Other) / Framing Type (Wood, Metal, Other) Depth (2 x 4, 2 x 6, other) Spacing (16” OC, 24” OC, other) |  |
| Cavity Ins At Ceiling: R-value, Thickness, Type (Batt, Spray, Blow, Other) Cavity Ins Below Roof Deck: R-value, Thickness, Type (Batt, Spray, Blow, Other) |  |
| Continuous Ins (indicate location such as below or above roof deck) R-value, Thickness, Type (Batt, Spray, Blow, Other) |  |
| Rad. Barrier: Y / N |  |
| Roofing: Cool Roof: Y / N Roofing product/specs: Air space below roofing material: Y / N |  |
| Roof Type #2 (new/altered/existing condition to be HERS verified): Type (Attic, Rafter, Other) / Framing Type (Wood, Metal, Other) Depth (2 x 4, 2 x 6, other) Spacing (16” OC, 24” OC, other) |  |
| Cavity Ins At Ceiling: R-value, Thickness, Type (Batt, Spray, Blow, Other) Cavity Ins Below Roof Deck: R-value, Thickness, Type (Batt, Spray, Blow, Other) |  |
| Continuous Ins (indicate location such as below or above roof deck) R-value, Thickness, Type (Batt, Spray, Blow, Other) |  |
| Rad. Barrier: Y / N |  |
| Roofing: Cool Roof: Y / N Roofing product/specs: Air space below roofing material: Y / N |  |
| Wall Type #1 (new/altered/existing condition to be HERS verified) Type (framed, mass, SIPS, other) / Framing Type (Wood, Metal, Other) Depth (2 x 4, 2 x 6, other) Spacing (16” OC, 24” OC, other) |  |
| Cavity Ins: R-value, Thickness, Type (Batt, Spray, Blow, Other) |  |
| Continuous Ins (indicate location) R-value, Thickness, Type (Batt, Spray, Blow, Other) |  |
| Wall Type #2 (new/altered/existing condition to be HERS verified) Type (framed, mass, SIPS, other) / Framing Type (Wood, Metal, Other) Depth (2 x 4, 2 x 6, other) Spacing (16” OC, 24” OC, other) |  |
| Cavity Ins: R-value, Thickness, Type (Batt, Spray, Blow, Other) |  |
| Continuous Ins: |  |
| Floor Type #1 (new/altered/existing condition to be HERS verified): Type (raised with crawlspace, no crawlspace, raised mass, unheated/heated slab on grade, other) Framing Type (Wood, Metal, Other) Depth (2 x 4, 2 x 6, other) Spacing (16” OC, 24” OC, other) |  |
| Cavity Ins: R-value, Thickness, Type (Batt, Spray, Blow, Other) |  |
| Slab Edge Continuous Ins (indicate location) R-value, Thickness, Type (Batt, Spray, Blow, Other) |  |
| Vertical Glazing Type #1 (new/altered/existing condition to be HERS verified) |  |
| Frame Type (wood, vinyl, metal;, thermally broken metal, other) Glazing Type (single, dual, triple, clear, tinted, low-e coating) |  |
| Rating (manufactured NFRC product, custom NFRC certified, non-NFRC rated) Manufacturer and series (if known) |  |
| Shading (solid and attached overhangs, sidefins) Elevation including shading (front, back left, right) |  |
| Vertical Glazing Type #2 (new/altered/existing condition to be HERS verified) |  |
| Frame Type (wood, vinyl, metal;, thermally broken metal, other) Glazing Type (single, dual, triple, clear, tinted, low-e coating) |  |
| Rating (manufactured NFRC product, custom NFRC certified, non-NFRC rated) Manufacturer and series (if known) |  |
| Shading (solid and attached overhangs, sidefins) Elevation including shading (front, back left, right) |  |
| Skylight Type (new/altered/existing condition to be HERS verified) |  |
| Frame Type (wood, vinyl, metal;, thermally broken metal, other) Glazing Type (single, dual, triple, clear, tinted, low-e coating) |  |
| Manufacturer and series (if known) |  |

| MECHANICAL EQUIPMENT |
| --- |
| Space Heating Type (new/altered/existing condition to be HERS verified) Fuel type (natural gas, propane, heat pump, electric resistance) System Type (packaged, split, hydronic, other) Output: Efficiency: # of systems and what areas of the home they are serving Manufacturer and model # (if known) | If new construction and gas heater installed, heat pump ready requirements will be required |
| Space Cooling Type (new/altered/existing condition to be HERS verified) Fuel type (heat pump, central air conditioning, swamp/evaporative cooler) System Type (packaged, split, hydronic, other) Output: Efficiency: # of systems and what areas of the home they are serving Manufacturer and model # (if known) |  |
| Ducts (new/altered/existing condition to be HERS verified) Location (Attic, Crawlspace, Conditioned Space, Garage , None (Such as ductless mini split, hydronic radiant floor or baseboard)) Altering ducting: Extending from existing to serve an addition, replacing/extending to serve existing home by altering __________ ft of ducting, N/A Insulation (None, R-4.2, R-6, R-8, Other) for existing, altered and new ducting |  |
| DHW (new/altered/existing condition to be HERS verified) Fuel type (natural gas, propane, standard heat pump, air-to-water heat pump, electric resistance) System Type (tank with ________ gallons, tankless, combined hydronic) Input: Efficiency: Recovery Efficiency: Manufacturer and model # (if known) Distribution (Standard, Parallel Piping, Point of Use, Recirc w/Pump Controls: Push Button / Motion sensor / None ) | If new construction and gas heater installed, heat pump ready requirements will be required |
| APPLIANCES |
| Cooktop Fuel type (natural gas, propane, induction, electric resistance) | If new construction and gas cooktop installed, electric ready requirements will be required |
| Dryer Fuel type (natural gas, propane, hear pump, electric resistance) | If new construction and gas dryer or gas hook ups installed, electric ready requirements will be required |

Project Information Worksheet

| Zone Information | Zone 1 | Zone 2 | Zone 3 |
| --- | --- | --- | --- |
| Zone Type/Name: |  |  |  |
| No. of Bedrooms: |  |  |  |
| CFA (ft²): |  |  |  |
| Building level (story): |  |  |  |
| Avg. ceiling ht (ft): |  |  |  |
| Elev. Above grade (ft): |  |  |  |
| Floor-to-floor ht (ft): |  |  |  |
| Window head ht (ft): |  |  |  |

| PV/Battery Information |
| --- |
| PV System: Y / N | Size (kWdc) | Azimuth | Tilt | Inverter Eff. | Solar Access % | CFI? |
| If not PV, and part of a subdivision with 10 or more homes, solar ready will be required |
| PV System Notes: |  |
| Battery Storage: Y / N | Capacity (kWh) | Control | Charging Eff. | Discharging Eff. | Self Utilization Credit? |
| If no battery installed of at least 5 KWH or higher, battery ready will be required |
| Battery Notes: |  |
| Envelope Information by Zone |
| Zone 1: | Front | Left | Rear | Right | Int. Wall >> | Int. Wall >> |
| Orientation (deg): |  |  |  |  |  |  |
| Wall area (ft²): |  |  |  |  |  |  |
| Window area (ft²): |  |  |  |  |  |  |
| Roof/ceiling area (ft²): |  | Pitch: |  | Skylight area (ft²): |
| Slab area (ft²): |  | Perimeter (ft): |  |  |  |
| Raised floor area (ft²): |  | Crawlspace perimeter (ft): |  |  |  |

| Envelope Information by Zone |
| --- |
| Zone 2: | Front | Left | Rear | Right | Int. Wall >> | Int. Wall >> |
| Orientation (deg): |  |  |  |  |  |  |
| Wall area (ft²): |  |  |  |  |  |  |
| Window area (ft²): |  |  |  |  |  |  |
| Door area (ft²): |  |  |  |  |  |  |
| Roof/ceiling area (ft²): |  | Pitch: |  | Skylight area (ft²): |
| Slab area (ft²): |  | Perimeter (ft): |  |  |
| Raised floor area (ft²): |  | Crawlspace perimeter (ft): |  |  |
| Envelope Information by Zone |
| Zone 3: | Front | Left | Rear | Right | Int. Wall >> | Int. Wall >> |
| Orientation (deg): |  |  |  |  |  |  |
| Wall area (ft²): |  |  |  |  |  |  |
| Window area (ft²): |  |  |  |  |  |  |
| Door area (ft²): |  |  |  |  |  |  |
| Roof/ceiling area (ft²): |  | Pitch: |  | Skylight area (ft²): |  |
| Slab area (ft²): |  | Perimeter (ft): |  |
| Raised floor area (ft²): |  | Crawlspace perimeter (ft): |  |  |

Energy Features Summary: Climate Zone ______

|  | Design for Prescriptive Compliance CZ: _______ Circle: New or Altered | Alternative B-1 New: As Designed by Client Alteration: Proposed Improvement | Alternative B-2 (Different than B-1) | Alternative B-3 (Different than B-2) |
| --- | --- | --- | --- | --- |
|  | Spec | Spec | Effect on Margin | Spec | Effect on Margin | Spec | Effect on Margin |
| EXAMPLE: Roof insulation | Vented Attic Roof Steep Slope: (6:12) Tile R-30 Insulation ceiling Radiant Barrier | Vented Attic Roof Steep Slope: (6:12) Tile R-49 Insulation ceiling Radiant Barrier | S.E.E -43.5 P.E.E – 42.6 +0.9 | Vented Attic Roof Steep Slope: (6:12) Tile R-38 Insulation ceiling R-13 Insulation at the Roof Deck | S.E.E -43.5 P.E.E – 42.3 +1.0 | Unvented Attic Roof Steep Slope: (6:12) Tile R-0 Insulation ceiling R-42 CCSPF Insulation at the Roof Deck | S.E.E -43.5 P.E.E – 41.2 +2.1 |
| Env | Roof insulation |  |  |  |  |  |  |  |
| Env | Roofing material |  |  |  |  |  |  |  |
| Env | Walls Exterior |  |  |  |  |  |  |  |
| Env | HERS |  |  |  |  |  |  |  |
| Env | Windows Efficiency |  |  |  |  |  |  |  |
| Env | Windows Shading |  |  |  |  |  |  |  |
| Mech | Heating: |  |  |  |  |  |  |  |
| Mech | Cooling: |  |  |  |  |  |  |  |
| Mech | IAQ |  |  |  |  |  |  |  |
| Mech | Distribution |  |  |  |  |  |  |  |
| Mech | DHW |  |  |  |  |  |  |  |
| Mech | DHW Tank Location |  |  |  |  |  |  |  |
| Mech | DHW Distribution |  |  |  |  |  |  |  |
| Mech | HERS |  |  |  |  |  |  |  |
| Battery | Flex Battery |  |  |  |  |  |  |  |
| PV | PV System |  |  |  |  |  |  |  |

Energy Features Summary: Climate Zone ______

|  | Design for Prescriptive Compliance CZ: _______ Circle: New or Altered | Alternative B-1 New: As Designed by Client Alteration: Proposed Improvement | Alternative B-2 (Different than B-1) | Alternative B-3 (Different than B-2) |
| --- | --- | --- | --- | --- |
|  | Spec | Spec | Effect on Margin | Spec | Effect on Margin | Spec | Effect on Margin |
| EXAMPLE: Roof insulation | Vented Attic Roof Steep Slope: (6:12) Tile R-30 Insulation ceiling Radiant Barrier | Vented Attic Roof Steep Slope: (6:12) Tile R-49 Insulation ceiling Radiant Barrier | S.E.E -43.5 P.E.E – 42.6 +0.9 | Vented Attic Roof Steep Slope: (6:12) Tile R-38 Insulation ceiling R-13 Insulation at the Roof Deck | S.E.E -43.5 P.E.E – 42.3 +1.0 | Unvented Attic Roof Steep Slope: (6:12) Tile R-0 Insulation ceiling R-42 CCSPF Insulation at the Roof Deck | S.E.E -43.5 P.E.E – 41.2 +2.1 |
| Env | Roof insulation |  |  |  |  |  |  |  |
| Env | Roofing material |  |  |  |  |  |  |  |
| Env | Walls Exterior |  |  |  |  |  |  |  |
| Env | HERS |  |  |  |  |  |  |  |
| Env | Windows Efficiency |  |  |  |  |  |  |  |
| Env | Windows Shading |  |  |  |  |  |  |  |
| Mech | Heating: |  |  |  |  |  |  |  |
| Mech | Cooling: |  |  |  |  |  |  |  |
| Mech | IAQ |  |  |  |  |  |  |  |
| Mech | Distribution |  |  |  |  |  |  |  |
| Mech | DHW |  |  |  |  |  |  |  |
| Mech | DHW Tank Location |  |  |  |  |  |  |  |
| Mech | DHW Distribution |  |  |  |  |  |  |  |
| Mech | HERS |  |  |  |  |  |  |  |
| Battery | Flex Battery |  |  |  |  |  |  |  |
| PV | PV System |  |  |  |  |  |  |  |

Energy Features Summary: Climate Zone ______

|  | Design for Prescriptive Compliance CZ: _______ Circle: New or Altered | Alternative B-1 New: As Designed by Client Alteration: Proposed Improvement | Alternative B-2 (Different than B-1) | Alternative B-3 (Different than B-2) |
| --- | --- | --- | --- | --- |
|  | Spec | Spec | Effect on Margin | Spec | Effect on Margin | Spec | Effect on Margin |
| EXAMPLE: Roof insulation | Vented Attic Roof Steep Slope: (6:12) Tile R-30 Insulation ceiling Radiant Barrier | Vented Attic Roof Steep Slope: (6:12) Tile R-49 Insulation ceiling Radiant Barrier | S.E.E -43.5 P.E.E – 42.6 +0.9 | Vented Attic Roof Steep Slope: (6:12) Tile R-38 Insulation ceiling R-13 Insulation at the Roof Deck | S.E.E -43.5 P.E.E – 42.3 +1.0 | Unvented Attic Roof Steep Slope: (6:12) Tile R-0 Insulation ceiling R-42 CCSPF Insulation at the Roof Deck | S.E.E -43.5 P.E.E – 41.2 +2.1 |
| Env | Roof insulation |  |  |  |  |  |  |  |
| Env | Roofing material |  |  |  |  |  |  |  |
| Env | Walls Exterior |  |  |  |  |  |  |  |
| Env | HERS |  |  |  |  |  |  |  |
| Env | Windows Efficiency |  |  |  |  |  |  |  |
| Env | Windows Shading |  |  |  |  |  |  |  |
| Mech | Heating: |  |  |  |  |  |  |  |
| Mech | Cooling: |  |  |  |  |  |  |  |
| Mech | IAQ |  |  |  |  |  |  |  |
| Mech | Distribution |  |  |  |  |  |  |  |
| Mech | DHW |  |  |  |  |  |  |  |
| Mech | DHW Tank Location |  |  |  |  |  |  |  |
| Mech | DHW Distribution |  |  |  |  |  |  |  |
| Mech | HERS |  |  |  |  |  |  |  |
| Battery | Flex Battery |  |  |  |  |  |  |  |
| PV | PV System |  |  |  |  |  |  |  |